## Slide 1
Demonstration Project
USB Link between Android tablet and VCOM device
Notes: https://www.freepik.com/free-vector/digital-marketing-landing-page_5467432.htm#page=1&query=marketing&position=8

## Slide 2
Content
CIO Presentation
Context introduction
Software Requirements
Development process
Delivery definition
Notes: https://www.freepik.com/free-vector/social-media-marketing-efficiency-promotion-report-mobile-phone-with-loudspeaker-data-graph_4102840.htm#page=5&position=4

## Slide 3: Présentation : CIO systèmes Embarqués
Specialized in embbeded systems (Software and Electronic)
Web site ciose.fr, contact : selso.liberado@ciose.fr
Founded : 1991
ISO9001 since 2019
1991
2000
2005
2013
2014
Création d’un bureau d’étude en informatique
Introduction de la compétence
Linux
Création d’un bureau d’étude en électronique
Développement du COM Hera
Ajout du nom commercial
CIOSE
2015
Introduction de la compétence FPGA
2019
ISO 9001
Sûreté de fonctionnement
Sécurité des systèmes

## Slide 4
Présentation : CIO systèmes Embarqués
Electronic studies
Signal processing
Audio, vidéo, DSP, FPGA
Low level development
BootLoader, drivers, BSP, Bare Metal
High level developement
GUI application
QT, visual C++, Androïd, iOS

## Slide 5: Requirements : context
The project is only intended to demonstrate ‘Proof of Concept’ (‘POC’).
The freelancer must reuse the supplied source.
We have created a sketch for the solution implementation.

## Slide 6: Requirements : Software requirements
The Mobile application reads and writes register to the device : Mobile is master, Device is slave.
All the protocol layer is implemented in the library, and reused in the mobile application and device.
The protocol is cleary divided in layers (device interface, frame R/W, register R/W).
Reliability : any connection loss is detected and can be re-established without restarting GUI/Device.
Performance : the connection must be established within 100 ms, and baudrate limited by the device performance (about 1 Mb / sec).
If the host does not support OTG, a notification is displayed when trying to enumerate devices.
Androit tablet
Samsung Galaxy Tab 10
GUI
Wrapped library
Coded in C
STM 32 Nucleo
Application
STMCube USB HAL
USB LINK

## Slide 7: System design Presentation
The GUI allows to test communication with the device throuh the library
The library implement a simple protocole (register R/W). Coded in C.
Wrapper allows integration with the final application.
The device is a non modified STM32 Nucleo F439ZI
We use the USB available interface for both tablet and device.
Androit tablet
Samsung Galaxy Tab 10
GUI
Wrapped library
Coded in C
STM 32 Nucleo
Application
STMCube USB HAL
USB LINK

## Slide 8: Design Presentation : about the Mobile Application
Mobile application, not webapp
Developped with Visual studion 2017
Using Microsoft Xamarin (C#)
Used the sub component Xamarin.forms
Library integration using Swig : (generate C# wrapper).

## Slide 9: Design Presentation : the library
Developped using C only.
Multi-platform compatibility (linux, windows)
Developped using QtCreator (PC) and Visual Studio 2017 (Android).
Standard calls are used for device access.

## Slide 10: Design Presentation : about the device
Nucleo STM32F439ZI
Developped using Atollic (STMCube IDE), STMCube MX, STMCube stack,
Using C99 standard
USB interface: VCOM port emulation.

## Slide 11: What’s already done ?
Mobile application :
  GUI done,
  library integration,
  Package Usb serial for Android was added for device recognition & CDC communication creation (but finally not used).
  We managed to Write/Write to the device Using USB Android API
Library : protocol implemented, with a pseudo device for test purpose (tested in the mobile app)
Library Wrapper : completed.
Device : completed. It acts as a device.
We have all sofware hosted on Github. It must be re-used.

## Slide 12: So what’s missing ?
We tried to pass the « fd » descriptor to the library : but an error occures (ENOENT)
Find the correct way to interact with the library :
  Preferred way : pass the Fd descriptor created in the C# context to the library that does all the job (search for the FIXME in the code).
  Accepted way : implement device’s R/W access in the C# context, use library calls for frame formating (write code)  We done this work and its working, so no need for you help.
  Refused way : bypass library and totally rewrite protocol in C#

## Slide 13: Developpement process : material & software
As the the material is very common we hope that you have what is required, but it can be discussed :
  Android Tablet (samsung galaxy tab 10, iWork, Lenovo…)
  STM32 Nucleo
  Direct male/male uUSB, or classic data uUSB câble with male to female adaptor.
Software : we just add you to the repo github.
Licence expected : LGPLv2

## Slide 14: Développement process : delivery
Code repository up to date
APK and binary delivered (release mode).
A report with all depedency listed an notes for explaining choices
Test report & some test benchmark.

## Slide 15: Développement process : validation
Code review
Rebuild solution
Test.